Sergio Coronado
16.484 Assignment # 2
Created :3/6/16
Due:	3/8/16

Objective:

The purpose of this assignment is to perform Fourier transforms on an image and apply a butter-worth low pass filter in the frequency domain.

Background:

This assignment is aimed at introducing image processing in the frequency domain. For the first part of the assignment the MRI image was transformed to the frequency domain using a 2d Fast Fourier transform algorithm. In the second part a second-order butters-worth low pass filter is applied in the frequency spectrum.

Algorithm Used:

The image was read in and a vectorized version of the image was created which had n* 2 columns. In the second part of the program the spectrum was then shifted by multiplying each pixel by (-1) ^ (x +y) . After the image has been vectorized it is then transformed using a 2D Fast Fourier transform. This was achieved by doing a 1D Fourier transform for each row of the vectorized image and then doing another 1D Fourier for each column in the in the image. Once the Fourier transform has completed the spectrum magnitude was calculated for both parts and normalized and sent to a output file. In the second part a low pass filter was applied to the the transformed image. Finally a the image is reverse using an inverse 2D Fast Fourier Transform.

Results:

The Program successfully transformed the image in into the frequency domain and back as required by the first part of the assignment as shown in figure 1. and figure 2.

Figure 1. Spectrum of MRI not centered	Figure 2. Reverse Image after IFFT

In the Second Part the spectrum was centered and the filter was applied successfully usign three different cutoff frequencies as shown in images

    Figure 3. Reduced MRI	Figure 4. Reduced Porsche

Conclusion and Observations

The exercise was successful in demonstrating images can be read and manipulated in program. As mentioned in the results the down-sampling of the image resulted a jagged quality in the image it might make a smoother image if for every other pixel the weighted average of the other intensities around was written into the output.

Readme

//////////////////////// Sergio Coronado Assignment 1 README /////////////////

////BUILD

 make sure theat both homework1a.c and homework1b.c have the variable CMD writte
 to be : /usr/X11R6/bin/xv when runnign on the anaconda machines

 $ make

///RUN

  bin/HW1a <input-file> <output-file> <xSize> <ySize>
  bin/HW1a <input-file> <output-file> <xSize> <ySize>

//Cleanup

  $ make clean
Code

  1 //////////////////////// homework1a.c /////////////////////////////////////////
  2 /*
  3 By: Sergio Coronado
  4 16.484 Computer Vision
  5 Assignemnt #1
  6 Part 1
  7
  8 PURPOSE:
  9 Program reads in an image specfied by user and outputs a file specified by user
 10 that has reduced to a quarter of the original size by keeping even pixels and
 11 discarding odd ones.
 12
 13 USAGE:
 14
 15 HW1a <input-file> <output-file> <xSize> <ySize>
 16
 17 */
 18
 19 ///////////////////////// Includes /////////////////////////////////////////////
 20
 21 #include <unistd.h>
 22 #include <stdio.h>
 23 #include <stdlib.h>
 24 #include <string.h>
 25 #include "CursorCntl.h"
 26 #include <sys/wait.h>
 27
 28 ///////////////////////// Constant Definitions /////////////////////////////////
 29
 30 #define SINGLE_BYTE 1
 31 #define HEADER_SIZE 20
 32 #define NUM_ARGS 3
 33 #define CMD_LENGTH 2
 34
 35 /* Command String for launching XV
 36 Note:
 37 For Runnign on School Lab this must be : /usr/X11R6/bin/xv
 38 */
 39
 40 //static char *CMD = "/usr/bin/xv";
 41 static char *CMD = "/usr/X11R6/bin/xv";
 42
 43 ///////////////////////// Function Prototypes //////////////////////////////////
 44
 45
 46 unsigned char ** ReadImage(
 47 FILE * openedFile, unsigned xSize, unsigned ySize, unsigned * numRows);
 48
 49 ///////////////////////// Main /////////////////////////////////////////////////
 50
 51 int main (int argc, char ** argv)
 52 {
 53 /////////////////////// Variables ////////////////////////////////////////////
 54
 55 unsigned char ** img; //Matrix Holding Image Values
 56 unsigned xSize; //NUmber of horizontal pixels
 57 unsigned ySize; //NUmber of vertical pixels
 58 unsigned numRows; //rows Read in
 59 unsigned char * zeroBuff; //Buffer used to mask image
 60 pid_t xvFork; //pid for xv launched
 61 char headerBuffer[HEADER_SIZE]; //array contianign header params for the image
 62 char * xvArgs[NUM_ARGS]; //Arguments for XV
 63 int status; ///Status variable
 64
 65
 66 FILE * openedFile; //File to be read In
 67 FILE * outputFile; //file to be written to
 68
 69 int i, j; //counter variables
 70
 71 /* Check correct n umber of arguments */
 72
 73 if (argc < 5)
 74 {
 75 printError("Invalid Parameters\n");
 76 exit (-1);
 77 }
 78
 79 /* Openede image File */
 80
 81 openedFile = fopen(argv[1], "r");
 82
 83 xSize = atoi(argv[3]);
 84
 85 ySize = atoi(argv[4]);
 86
 87 if (openedFile == NULL)
 88 {
 89 printError("Error Could Not Open file\n");
 90 exit (-1);
 91 }
 92
 93 img = (unsigned char **) malloc( sizeof(unsigned char *) * ySize);
 94
 95 zeroBuff = (unsigned char *) calloc (xSize/2, sizeof(unsigned char ));
 96
 97 printOK("Reading Image\n");
 98
 99 /* Read Image */
100
101 img = ReadImage(openedFile, xSize, ySize, &numRows);
102
103 /* Close input file and open output file */
104 /* Designed in this order in case user wishes to over-write image */
105
106 fclose(openedFile);
107
108 outputFile = fopen(argv[2], "w");
109
110 printOK("Building Image\n");
111
112 sprintf(headerBuffer, "P5\n%d %d\n255\n", xSize, ySize);
113
114 fwrite(headerBuffer, sizeof(unsigned char), strlen(headerBuffer), outputFile);
115
116 for ( i = 0; i < numRows; i++)
117 {
118 /* Write the first half of the row as blank then write the second half
119 from the read-in image */
120
121 fwrite( zeroBuff, sizeof(unsigned char), xSize/2, outputFile);
122 for (j = xSize/2 ; j < xSize; j ++)
123 {
124 fwrite(&img[i][j], sizeof(unsigned char), SINGLE_BYTE, outputFile);
125 }
126 }
127
128 fclose(outputFile);
129
130
131 printOK("Image Built Starting XV\n");
132
133 xvArgs[0] = CMD;
134 xvArgs[1] = argv[2];
135 xvArgs[2] = NULL;
136
137 xvFork = fork();
138
139 if (xvFork == 0)
140 {
141 status = execv(CMD, xvArgs);
142 if (status < 0)
143 {
144 printError("Could Not Initiate XV\n");
145 }
146
147 }
148 else
149 {
150 waitpid(xvFork, 0, 0);
151 }
152
153 return 0;
154
155 }
156
157
158 ///////////////////////// ReadImage() //////////////////////////////////////////]
159 /*
160 PURPOSE
161 The read image function reads an image from a file of size specified in the
162 parameters
163 INPUT
164 FILE * openedFile : pointer to the file being opened must be opened priot to
165 call
166 unsigned xSize ` : number of columns in image to be read
167 unsigned ySize : number of rows in image to be read
168 unsigned char *** img : Pointer to be set to the
169
170 OUTPUT
171
172 unsigned char ** img : read-in matrix of pixel densities
173
174 */
175
176 unsigned char ** ReadImage(
177 FILE * openedFile, unsigned xSize, unsigned ySize, unsigned * numRows)
178 {
179 unsigned char ** img; //pointer to hold the address of the image matrix
180 unsigned bytesRead; // variable counting the bytes read per line
181 unsigned i, j; // COUNTER VARIABLES
182
183 *(numRows) = 0;
184
185 img = (unsigned char **) malloc( sizeof(unsigned char *) * ySize);
186
187 for ( i = 0; i < ySize; i ++)
188 {
189 img[i] = (unsigned char *) malloc (sizeof(unsigned char) * xSize);
190 bytesRead = fread(img[i], sizeof(unsigned char), xSize , openedFile );
191 if (bytesRead < xSize)
192 {
193 if (feof(openedFile))
194 {
195 printWarning("Reached Unexpected EOF Attemptin padding to size\n");
196 for (j = (bytesRead -1); j < xSize; j++)
197 {
198 img[i][j] = 0;
199 }
200 }
201 else
202 {
203 printError("Error Reading File");
204 }
205
206 }
207 *(numRows) += 1;
208
209 }
210 return img;
211 }
  1 ///////////////////////// homework1b.c /////////////////////////////////////////
  2 /*
  3 By: Sergio Coronado
  4 16.484 Computer Vision
  5 Assignemnt #1
  6 Part 2
  7
  8 PURPOSE:
  9 Program reads in an image specfied by user and outputs a file specified by user
 10 that has reduced to a quarter of the original size by keeping even pixels and
 11 discarding odd ones.
 12
 13 USAGE:
 14
 15 HW1b <input-file> <output-file> <xSize> <ySize>
 16
 17 */
 18
 19 ///////////////////////// Includes /////////////////////////////////////////////
 20
 21
 22 #include <unistd.h>
 23 #include <stdio.h>
 24 #include <stdlib.h>
 25 #include <string.h>
 26 #include "CursorCntl.h"
 27 #include <sys/wait.h>
 28
 29 ///////////////////////// Constant Definitions /////////////////////////////////
 30
 31 #define SINGLE_BYTE 1
 32 #define HEADER_SIZE 20
 33 #define NUM_ARGS 3
 34 #define CMD_LENGTH 2
 35
 36 /* Command String for launching XV
 37 Note:
 38 For Runnign on School Lab this must be : /usr/X11R6/bin/xv
 39 */
 40
 41 //static char *CMD = "/usr/bin/xv";
 42 static char *CMD = "/usr/X11R6/bin/xv";
 43
 44 ///////////////////////// Function Prototypes //////////////////////////////////
 45
 46
 47 unsigned char ** ReadImage(
 48 FILE * openedFile, unsigned xSize, unsigned ySize, unsigned * numRows);
 49
 50 ///////////////////////// Main /////////////////////////////////////////////////
 51
 52
 53 int main (int argc, char ** argv)
 54 {
 55
 56 /////////////////////// Variables ////////////////////////////////////////////
 57
 58
 59 unsigned char ** img; //Matrix Holding Image Values
 60 unsigned xSize; //NUmber of horizontal pixels
 61 unsigned ySize; //NUmber of vertical pixels
 62 unsigned numRows; //rows Read in
 63 pid_t xvFork; //pid for xv launched
 64 char headerBuffer[HEADER_SIZE]; //array contianign header params for the image
 65 char * xvArgs[NUM_ARGS]; //Arguments for XV
 66 int status; //Status variable
 67
 68
 69 FILE * openedFile; // file to be read in
 70 FILE * outputFile; // file to be wrtten out
 71
 72 int i, j; //counter varaibles
 73
 74 /* Check Correct number of argumetns */
 75
 76 if (argc < 5)
 77 {
 78 printError("Invalid Parameters\n");
 79 exit (-1);
 80 }
 81
 82 /* open image file */
 83
 84 openedFile = fopen(argv[1], "r");
 85
 86 xSize = atoi(argv[3]);
 87
 88 ySize = atoi(argv[4]);
 89
 90 if (openedFile == NULL)
 91 {
 92 printError("Error Could Not Open image file\n");
 93 exit (-1);
 94 }
 95
 96 numRows = 0;
 97
 98 printOK("Reading Image\n");
 99
100 /* Read Image */
101
102 img = ReadImage( openedFile, xSize, ySize, &numRows);
103
104 /* Close input file and open output file */
105 /* Designed in this order in case user wishes to over-write image */
106
107 fclose(openedFile);
108
109 outputFile = fopen(argv[2], "w");
110
111 if (outputFile == NULL)
112 {
113 printError("Could Not Open or create ouput file\n");
114 exit (-1);
115 }
116
117 printOK("Building Image\n");
118
119 sprintf(headerBuffer, "P5\n%d %d\n255\n", xSize/2, ySize/2);
120
121 fwrite(headerBuffer, sizeof(unsigned char), strlen(headerBuffer), outputFile);
122
123 for ( i = 0; i < numRows; i += 2)
124 {
125 for (j = 0 ; j < xSize; j += 2)
126 {
127 fwrite(&img[i][j], sizeof(unsigned char), SINGLE_BYTE, outputFile);
128 }
129 }
130
131 fclose(outputFile);
132
133 printOK("Image Built Starting XV\n");
134
135 xvArgs[0] = CMD;
136 xvArgs[1] = argv[2];
137 xvArgs[2] = NULL;
138
139 xvFork = fork();
140
141 if (xvFork == 0)
142 {
143 status = execv(CMD, xvArgs);
144 if (status < 0)
145 {
146 printError("Could Not Initiate XV\n");
147 }
148
149 }
150 else
151 {
152 waitpid(xvFork, 0, 0);
153 }
154
155 return 0;
156
157 }
158
159 ///////////////////////// ReadImage() //////////////////////////////////////////]
160 /*
161 PURPOSE
162 The read image function reads an image from a file of size specified in the
163 parameters
164 INPUT
165 FILE * openedFile : pointer to the file being opened must be opened priot to
166 call
167 unsigned xSize ` : number of columns in image to be read
168 unsigned ySize : number of rows in image to be read
169 unsigned char *** img : Pointer to be set to the
170
171 OUTPUT
172
173 unsigned char ** img : read-in matrix of pixel densities
174
175 */
176
177 unsigned char ** ReadImage(
178 FILE * openedFile, unsigned xSize, unsigned ySize, unsigned * numRows)
179 {
180 unsigned char ** img; //pointer to hold the address of the image matrix
181 unsigned bytesRead; // variable counting the bytes read per line
182 unsigned i, j; // COUNTER VARIABLES
183
184 *(numRows) = 0;
185
186 img = (unsigned char **) malloc( sizeof(unsigned char *) * ySize);
187
188 for ( i = 0; i < ySize; i ++)
189 {
190 img[i] = (unsigned char *) malloc (sizeof(unsigned char) * xSize);
191 bytesRead = fread(img[i], sizeof(unsigned char), xSize , openedFile );
192 if (bytesRead < xSize)
193 {
194 if (feof(openedFile))
195 {
196 printWarning("Reached Unexpected EOF Attemptin padding to size\n");
197 for (j = (bytesRead -1); j < xSize; j++)
198 {
199 img[i][j] = 0;
200 }
201 }
202 else
203 {
204 printError("Error Reading File");
205 }
206
207 }
208 *(numRows) += 1;
209
210 }
211 return img;
212 }